## Slide 1
Streaming Middleware Bridge (gRPC) — Component 2 of 4
The only stateful, real-time component. Turns live forked call audio into scored analysis windows inside a 500 ms budget, for ~1,200 concurrent calls — on a stream that cannot be paused.
(1) TELEPHONY &
MEDIA GATEWAY
FreeSWITCH + mod_audio_stream
SIP / RTP · forks call audio
thread-isolated per channel
(2) STREAMING BRIDGE
gRPC
MY COMPONENT
normalise · session state ·
buffer · window · transport
reorder · fan-out · degrade
(3) AI & DSP ENGINE
WavLM + LFCC/MGD fusion
Silero VAD · ECAPA-TDNN
RTF <= 0.1 target
dev EER 0.55% (in-domain)
(4) RISK ENGINE
+ DASHBOARD
weighted multi-signal fusion
dynamic thresholds
prevention + CRM webhooks
WS · L16
windows
scores
results
FOUR INTERFACE CONTRACTS — agree these before anyone writes code; changing one later costs all four of us
CONTRACT A
Gateway -> Bridge
session_id server-issued or HMAC-signed
encoding L16_LE / L16_BE / PCMU / PCMA
sample_rate 8000 or 16000 — never assumed
channels + leg mono only; 2 legs = 2 sessions
sample_offset the authoritative clock
concealed true if gateway invented the audio
consent DPDP gate — no consent, no audio
OPEN Q is your L16 big- or little-endian?
Byte-swapped PCM is loud noise, and
the detector will confidently call it
synthetic. Validated by a 1 kHz test
tone in the session-open handshake.
CONTRACT B
Bridge <-> AI Engine (gRPC)
AudioChunk pcm, window_seq, sample_offset
gap_before, partial, session_epoch
RiskScoreUpdate window_seq ECHOED back
model_version, status
why echoed out-of-order results are otherwise
unrecoverable on my side
batch always 1 — Dhwani collapses batches
deadline 400 ms per window; on breach the
window is ABANDONED, never retried —
a late score is worthless and the
retry steals capacity from fresh audio.
pooling 80 streams/conn (HTTP/2 caps at 100)
CONTRACT C
Bridge -> Risk Engine
ordering monotonic window_seq, deduplicated
gaps gap_before=true resets smoothing
status OK / SKIPPED_SILENCE / DEGRADED
/ DETECTOR_UNAVAILABLE
critical a missing signal must renormalise,
never be substituted with 0.0
model_version never mix versions in one call
OPEN Q on DETECTOR_UNAVAILABLE, do you
renormalise over remaining signals or
hold the last score? Treating a missing
signal as 0.0 fabricates fraud signal.
cadence 10 scores/sec at L0, fewer when degraded
CONTRACT D
Bridge -> Dashboard
transport best-effort WebSocket
delivery lossy by design
rule never in the critical path
must never apply backpressure
that reaches the audio path
reconnect client resumes, no server state
cardinality no per-session metric labels
why lossy a dashboard that can slow the audio
path is a dashboard that can drop
fraud detection. It gets best-effort
delivery and no guarantees, forever.
payload score, status, model_version, seq
CORE CONSTRAINT Every other service in this system can tell its upstream to slow down. A phone call cannot be paused.
Everything else — the ring buffer, the drop-oldest policy, the adaptive hop, the whole degradation ladder — is a consequence of that one fact.

## Slide 2
Inside the Bridge — Eight Stages, One Timeline
N dissimilar transports become one canonical PCM timeline; that timeline becomes fixed windows the model was trained to expect.
FreeSWITCH
WebSocket · L16 binary
8 or 16 kHz · primary path
Asterisk
TCP · AudioSocket
length-prefixed framing
Twilio
WSS · base64 JSON
G.711 mu-law 8 kHz
INGRESS
ADAPTERS
N formats -> 1 frame
decode · mono · 16 kHz
soxr VHQ resample
endianness validated
identical to training path
SESSION
MANAGER
lifecycle + fencing
Redis epoch token
consent gate (DPDP)
resume within 15 s
2nd claimant rejected
RING
BUFFER
bounded 256 KB
jitter absorb 60 ms
drop OLDEST on full
never blocks ingest
1 producer, 1 consumer
WINDOWER
2.0 s / 100 ms hop
sample-accurate
VAD-gated (~40% saved)
len from checkpoint
hop by samples, not frames
gRPC
POOL
bidi stream, batch=1
conn pool: 80 streams
400 ms deadline
retry on NEW stream
keepalive < LB idle
REORDER
by window_seq
300 ms bounded wait
FAN-OUT
dedupe · annotate gaps
risk / dash / CRM
(4) RISK ENGINE
weighted fusion
prevention actions
scores
THREE DECISIONS THAT DETERMINE WHETHER THIS SCALES
CONCURRENCY
One asyncio loop. No per-session threads.
1,200 threads costs ~9.6 GB of stack before any audio is buffered, and collapses on context switching. Sessions are coroutines; each ring has exactly one producer and one consumer, so it needs no lock.
CPU work (resample, VAD) runs in a process pool — a 5 ms block on the loop x 1,200 sessions is 300 s of stall per second.
Verified by: 1,200 concurrent sessions held for 30 min inside the latency budget.
THE CLOCK
sample_offset is authoritative — not wall time.
Wall clocks drift, jump on NTP, and differ per pod. A gateway running at 8000.5 Hz against an assumed 8000 Hz accumulates 1.8 s of error per hour.
Windowing must be reproducible: the same audio must produce the same windows regardless of when packets happened to arrive. Wall clock is used only to measure the SLA.
Verified by: sample_offset stays monotonic across an injected 300 ms gap and a reconnect.
MEMORY
256 KB per session, enforced.
4 s ring x 16 kHz x 4 bytes = 256 KB. At 1,200 concurrent sessions that is ~300 MB — comfortable.
The same design with an unbounded per-session accumulator over a 1-hour call would be 690 GB.
Verified by: 8-hour soak at 200 sessions — any upward memory slope is a per-session leak.

## Slide 3
Latency, Failure Handling & the Edge Cases That Fail Silently
Most failures are loud, and therefore cheap. The expensive ones produce plausible-looking numbers that are wrong.
500 ms END-TO-END SLA caller speaks -> score delivered
60
100
200
65
jitter buffer 60 ms · window fill 100 ms · inference 200 ms · slack 65 ms
Inference is 46% of the entire budget — so jitter-buffer depth is my single biggest lever before I must start dropping windows.
Every stage is measured separately. One end-to-end number cannot tell you which of the four of us regressed, and each of us will assume it was one of the other three.
Time-to-first-score is ~2.4 s, not 500 ms — a full 2 s window must exist before anything can be scored.
OPERATING-POINT TARGETS reported by name, not as an abstract EER
FAR < 1.5% synthetic voices that get through FRR < 3.0% genuine callers wrongly flagged
RTF <= 0.1 1 s of audio processed in <= 100 ms E2E < 500 ms conversational turn-taking budget
Current fusion model measures FAR 0.55% / FRR 0.55% in-domain — both inside target, but not yet validated out-of-domain.
DEGRADATION LADDER hysteretic: exit only after 10 s of health
L0 NORMAL 2 s window / 100 ms hop · full cadence
L1 ELEVATED queue > 2 windows -> hop widens to 200 ms
L2 DEGRADED ring dropping -> hop 500 ms, drop oldest
L3 DETECTOR DOWN gRPC gone > 5 s -> scoring stops, call lives
L4 SHEDDING node at capacity -> reject NEW sessions only
GOVERNING RULE absence of a score is never equivalent to a low score.
Reporting “genuine” when the pipeline is broken is the one failure mode that actively causes harm.
THE THREE THAT FAIL SILENTLY — no exception, no error, just quietly wrong output. 71 edge cases catalogued in total.
AU-04 AUDIO
Averaging a dual-leg fork
The gateway forks caller and callee as two channels. Averaging them mixes two speakers into one signal, destroying both the deepfake and the speaker-verification signal.
FIX mono mandatory. Two legs arrive as two sessions sharing a call_id. Reject 2-channel input outright — never average.
TEST assert channels == 1 at the ingress adapter; a 2-channel fixture must raise.
COST IF MISSED every score on every dual-leg call is meaningless, and nothing anywhere reports an error.
AU-08 AUDIO
Packet-loss concealment
On a bad line the gateway invents audio to cover lost packets. That audio is literally synthetic — so the detector flags a genuine caller as a deepfake.
FIX gateway sets concealed=true; windows over ~15% concealed samples are skipped or sent with a down-weight flag.
TEST replay at 30% packet loss with PLC on — false-positive rate must not rise.
COST IF MISSED genuine customers on poor lines get accused of fraud. This is what gets the system switched off.
SS-06 SESSION
Missing speaker enrolment
No reference voiceprint makes similarity return 0.0, which fusion reads as 'total mismatch' — fabricating fraud signal for every caller who never enrolled.
FIX emit null plus speaker_signal=UNAVAILABLE. The risk engine renormalises over remaining signals.
TEST an unenrolled caller must not score higher than an enrolled match baseline.
COST IF MISSED every first-time caller looks like an impostor — false accusations at the worst possible moment.